## Slide 1: Sobriety Classification Using Gait and Other Biometrics
Kevin Martin & Ravjot Sachdev
Department of Electrical Engineering and Computer Science
9/9/2020

## Slide 2: Sobriety Detection Using Machine Learning
  Two-step biometric system to detect sobriety levels
  First step involves gait-measurement as recorded by phone telemetry data
    Data is processed via machine learning algorithms
    Data is collected via passive methods
  Second step involves iris scanning to confirm sobriety levels
    Data would be collected through active methods
Department of Electrical Engineering and Computer Science
Rolling average of x axis vs. TAC reading

## Slide 3: Background/Previous Works
Manual testing
  SFSTs (walk-and-turn, one leg stand)
  Breathalyzers
Gait
  Measurements: 3-axis accelerometer, gyroscope, magnetometer
  Features: Mean, standard deviation, correlation, energy
  Ascending limb vs descending limb
  Optical flow analysis using video
Eye thermal imaging
  Features: Ratio of mean value of iris pixels to mean value of sclera pixels
Department of Electrical Engineering and Computer Science
Eye thermal imaging
Left: sober, Right: drunk

## Slide 4: Overview of experiment design
Feature Extraction:
  TAC readings measured every half hour, telemetry readings measured every millisecond
  Used three sets of moving averages (500, 1000, 5000) for all three axes (x, y, and z)
  Matched rolling averages to TAC readings, leaving over 5,000 records to test
Department of Electrical Engineering and Computer Science

## Slide 5: Overview of experiment design - continued
Methodology:
  Split TAC readings into binary groups: >=.08 inebriated, <.08 sober
  Tested multiple machine learning algorithms to determine the most effective: naïve Bayes, decision tree, grid search, and XGBoost
  Utilized scikit-learn API in Python with a 70/30 train test split
  Created a “driver” function to test each model on the same x and y data each time
Department of Electrical Engineering and Computer Science

## Slide 6: Results
Focused on accuracy, with a secondary emphasis on precision and recall
XGBoost performed the best, with almost 99% accuracy
Grid search was second best, but required much more setup/tuning
  Costs outweighed the benefits, especially when considering how well XGBoost works “out of the box”
Department of Electrical Engineering and Computer Science

## Slide 7: Results Comparisons
Facial thermal imaging
  87% accuracy
  Bayesian classifier
Eye thermal imaging
  “99% confidence”
  Undetermined for 5 of 41 participants
  Supervised learning - Support Vector Machine (SVM)
Gait
  Accelerometer – Different training data for ascending/descending limb
    Bayesian Regularized Neural Network and Fast Fourier Transformation
  Video – near 100% accuracy
Department of Electrical Engineering and Computer Science
Optical flow frames

## Slide 8: Conclusion/Future Work
We would like to implement the second step of our system and use iris scanning to help confirm the results of the telemetry models
  Would require extra hardware for thermal imaging
We would also like to extend the initial step by including more test subjects and control for external variables
Overall, we are pleased with the results from the first step and believe we have demonstrated it is possible to accurately determine sobriety levels from biometric data
Department of Electrical Engineering and Computer Science

## Slide 9: Questions/Comments
Department of Electrical Engineering and Computer Science